## Slide 1: Apache Kafka vs MQTT
Hung Pham, Software Engineer

## Slide 2: Agenda
What is Apache Kafka?
Advantages of Kafka
Disadvantages of Kafka
What is MQTT?
Advantages of MQTT
Disadvantages of MQTT
Kafka vs MQTT comparision
Discussion

## Slide 3: What is Apache Kafka?
  Apache Kafka is a distributed event streaming platform designed for high-throughput, real-time data pipelines and streaming applications. It is commonly used for log aggregation, event sourcing, messaging systems, and streaming analytics.

## Slide 4: Advantages of Kafka
Mesa Confidential
  High Throughput and Scalability: Kafka is designed for high-throughput message processing, capable of handling millions of messages per second. It scales horizontally by adding more brokers, making it highly suitable for large-scale applications.
  Durability and Persistence: Kafka stores messages on disk, allowing for long-term retention. This ensures data is available even if consumers go offline. Messages are persisted with configurable retention periods, providing fault tolerance and durability.
  Stream Processing Capabilities: Kafka Streams allows for real-time stream processing, enabling transformations, filtering, and aggregations directly on streams. well with stream processing frameworks like Apache Flink and Apache Spark.
  Exactly-Once Semantics: Kafka provides exactly-once semantics, ensuring that messages are processed exactly once, which is critical in financial services, data pipelines, etc.
  Distributed Architecture: - Kafka’s distributed nature provides high availability and fault tolerance with replication across multiple nodes, making it reliable for critical applications.
  Ecosystem and Integrations: Kafka has a broad ecosystem of connectors (Kafka Connect) and clients for various programming languages. Well-integrated with big data platforms like Hadoop, Spark, and data lake architectures.

## Slide 5: Disadvantages of Kafka
Mesa Confidential
  Complexity in Setup and Maintenance: Kafka’s distributed architecture can be complex to set up, configure, and maintain, especially when scaling clusters. Requires careful tuning of parameters such as replication, partitions, and retention policies for optimal performance.
  Latency: Kafka is designed for high-throughput over low-latency. While it is fast, it may not be suitable for ultra-low latency applications (like real-time IoT control systems).
  Heavy Resource Consumption: Kafka requires significant resources (memory, CPU, and disk) to manage high-throughput workloads, particularly for large deployments.
  No Native Support for Lightweight Devices: Kafka is not designed for low-power devices (like sensors or embedded systems) as it relies on heavier networking and data handling mechanisms.

## Slide 6: What is MQTT?
Message Queuing Telemetry Transport (MQTT) is a lightweight messaging protocol designed for constrained devices and low-bandwidth, high-latency, or unreliable networks. It is widely used in IoT (Internet of Things) applications.

## Slide 7: Advantages of MQTT
Mesa Confidential
  Low Bandwidth and Lightweight: MQTT is designed to operate in low-bandwidth, high-latency networks, making it highly efficient for IoT devices. Its simple and small protocol overhead makes it suitable for constrained environments such as sensors and mobile devices.
  Efficient for Small Devices: MQTT is optimized for devices with limited processing power and memory, such as embedded systems, making it the de facto choice for IoT. It supports QoS (Quality of Service) levels to guarantee message delivery even in unreliable network conditions.
  Simple and Easy to Implement: MQTT is simpler to implement and deploy, especially for applications involving lightweight devices and sensors. Client libraries are available for many programming languages and IoT platforms.
  Low-Latency Messaging: MQTT is ideal for low-latency, near real-time messaging. It uses a publish-subscribe model, which is effective for applications requiring instant message delivery (e.g., real-time monitoring).
  Persistent and Retained Messages: MQTT brokers can retain messages for clients that are offline, ensuring that data is not lost even if the client temporarily disconnects.

## Slide 8: Disadvantages of MQTT
Mesa Confidential
  Designed for High Throughput: MQTT is designed for lightweight, low-bandwidth scenarios, so it struggles with high-throughput or large-scale data pipelines. It’s less suitable for applications requiring millions of messages per second or large payloads.
  Limited Data Persistence: While MQTT can retain messages, it does not natively support long-term storage or high-throughput persistence like Kafka. It relies on external systems for data retention.
  Limited Stream Processing: MQTT is primarily a messaging protocol and does not natively support advanced stream processing capabilities like Kafka Streams.
  Reliability Challenges: While MQTT supports QoS levels for message delivery guarantees, it does not offer the same level of durability and fault tolerance as Kafka (e.g., no replication between brokers).
  No Support for Complex Event Processing: MQTT lacks built-in support for complex event processing, windowing, or transformations, which are common in streaming data platforms like Kafka.

## Slide 9: Kafka vs MQTT Comparision
Mesa Confidential
Feature | Kafka | MQTT
Use Case | High-throughput, distributed, real-time streaming data (logs, events, analytics) | Low-latency, lightweight messaging for IoT, sensor networks
Data Throughput | High throughput (millions of messages per second) | Low throughput (small payloads, low message rate)
Latency | Low-to-moderate (not ideal for ultra-low latency) | Very low latency (ideal for real-time IoT control)
Durability | High durability with persistence on disk | Limited durability, relies on QoS levels and retained messages
Complexity | Complex setup and management (requires tuning and resource allocation) | Simple to implement and deploy for lightweight devices
Stream Processing | Built-in (Kafka Streams) or via external frameworks | No native stream processing
Scalability | Horizontally scalable with distributed brokers | Limited scalability for lightweight devices
Data Retention | Configurable, supports long-term storage | Limited, retention for offline clients only
Protocol Type | Message broker, distributed log-based system | Lightweight messaging protocol, publish-subscribe

## Slide 10: Kafka vs MQTT Comparision Cont…
Mesa Confidential
Choose Kafka when… | Choose MQTT when…
You need a high-throughput system capable of handling real-time streaming data. You require data durability, persistence, and the ability to replay events. Stream processing is a critical part of your arcshitecture, and you need the flexibility to process large volumes of data. You are working with distributed systems where fault tolerance and scalability are necessary. | You are dealing with IoT, sensor networks, or other scenarios where lightweight communication and low power consumption are essential. You need low-latency communication for small messages with simple publish-subscribe patterns. You prioritize ease of implementation and want a minimalistic protocol for constrained environments. You are working in environments with low bandwidth or unstable network conditions where guaranteed message delivery is important.
In summary, Kafka excels in high-throughput, distributed streaming scenarios, while MQTT is better suited for lightweight, low-latency IoT applications.
The most popular MQTT brokers and platforms are widely adopted due to their reliability, scalability, ease of use, and suitability for IoT use cases.

## Slide 11
Mesa Confidential